STM5600D (digital) Monitor Features

- Digital / 307,000 pixels

- LED Backlit LCD Panel, Last 5 times Longer than other LCDs

- Immunity to Vibration, Standard LCD Panels can Lose 50% Life

- 60% Better Light Output in Cold Weather Than Std. LCD Panels

- Auto-On When Vehicle is Placed in Reverse

- High Resolution, Low Reflection TFT LCD

- Works with 10V-32V Power Sources

- 3 Camera Inputs

- Day / Night Mode

- Contrast Control

- Brightness Control

- Built in Speaker

- 2 Year Limited Warranty

CC77 Camera Features

- “SONY SUPER HAD” Ultra Low Light 1/3" Interline Transfer Color CCD Sensor

- Built-in Heater w/ auto activation at 32 degrees F

- Electronic Auto Iris Control

- High Output Infra-Red LEDs

- Auto White Balance

- Back Light Compensation

- G-Force Rating = 10G (highest possible rating)

- 100% Waterproof (OK to pressure wash)

- Normal / Mirror Mode Switch on back of Camera

- Lux rating: 0.1 lux / Infra-Red on 0.0 Lux

- Built in Microphone

- 270,000 Pixels

- 2 Year Limited Warranty

| Color LCD Monitor | Specifications |
| --- | --- |
| Rated Voltage | 12Volt DC, Negative Ground |
| Operating Voltage | 10 to 32 Volts DC |
| Current Consumption | 1.7 Amperes |
| TV System | EIA |
| Picture Type | Color TFT LCD-Digital |
|  | 5.6" Diagonally |
| OSD | On Screen Display Functions |
| Picture Image | Factory Preset to Reverse Image |
| Picture Resolution | 307,000 pixel |
| Power Connector | Red: Positive (10-32V) |
|  | Green: Reverse Gear Input (10-32V) |
|  | Black: Ground |
| Inputs | 4-Pin Mini Jack |
|  | (1) Video input: 1.0V p-p,75ohm sync negative |
|  | (2) Audio |
|  | (3) DC 12 Volt, 0.2A DC (output) |
|  | (4) Ground |
| Power Requirements | 10Volts to 32 Volts DC |
| Power Consumption | 20W Maximum |
| Operating Temperature | -10 C to + 60C (+5 F to +140 F) |
| Storage Temperature | -15 C to +85 C (-17F to +185 F) |
| Dimensions | 6.25 (W) x 4.5 (H) x 1.2 (D) inches |
| Weight Approx. | .8 lbs |
| Design and specifications are subject to change. | Design and specifications are subject to change. |
| Camera | Specifications |
| Signal System | EIA |
| Image Sensor | SONY SUPER HAD 1/3" Color CCD |
| Picture Elements | 270,000 Pixels |
| Viewing Angle | 130 Degrees (Diag.) 121 (H) 90 (V) |
| Outer Dimensions | 2.5 (W) x 1.5 (H) x 2.5 (D) inches |
| Low Light Enhancement | Infra-Red Lights |
| Lux. Rating | 0.00 lux w/IP On |
| Audio | Built in Microphone |
| Housing | Lightweight Aluminum Die Cast |
| Vibration Rating | 10G (best possible rating) |
| Operating Temperature | -50F – +165 |