Monitor Features

- Auto-On When Vehicle is Placed in Reverse

- High Resolution, Low Reflection TFT LCD

- Works with 10V-32V Power Sources

- Day / Night Mode

- Contrast Control

- Brightness Control

- Built in Speaker

Camera Features

- This camera has been tested and proven to provide outstanding protection against water under severe conditions.

- 1/3" Interline Transfer Color CCD Sensor

- Electronic Auto Iris Control

- Low Illumination Image Sensor

- Auto White Balance

- Back Light Compensation

- G-Force Rating = 10 (highest possible rating)

- 100% Waterproof

- Normal / Mirror Mode Switch on back of Camera

- Lux rating: 0.1 lux / IR on 0.001 Lux

- Built in Microphone

- 270,000 Pixels

- Stainless Steel Mounting Hardware

| Color LCD Monitor | Specifications |
| --- | --- |
| Rated Voltage | 12Volt DC, Negative Ground |
| Operating Voltage | 10 to 32 Volts DC |
| Current Consumption | 1.7 Amperes |
| TV System | EIA |
| Picture Type | Color TFT LCD |
|  | 7.0" Diagonally |
| OSD | On Screen Display Functions |
| LCD Viewing Angle | 60/60/40/60 |
| Picture Resolution | 270,000 pix |
| Power Connector | Red: Positive (10-32V) |
|  | Green: Reverse Gear Input (10-32V) |
|  | Black: Ground |
| Inputs | 4-Pin Mini Jack |
|  | (1) Video input: 1.0V p-p,75ohm sync negative |
|  | (2) Audio |
|  | (3) DC 12 Volt, 0.2A DC (output) |
|  | (4) Ground |
| Power Requirements | 10Volts to 32 Volts DC |
| Power Consumption | 20W Maximum |
| Operating Temperature | -10 C to + 60C (+5 F to +140 F) |
| Storage Temperature | -15 C to +85 C (-17F to +185 F) |
| Dimensions | 7.25 (W) x 5.25 (H) x 1.2 (D) inches |
| Weight Approx. | 1.0 lb |
| Design and specifications are subject to change. | Design and specifications are subject to change. |
| Camera | Specifications |
| Signal System | EIA |
| Image Sensor | "Sony HAD" 1/3" Color CCD w/ Electronic Auto-Iris |
| Picture Elements | 270,000 Pixels |
| Viewing Angle | 130 Degrees (Diag.) 121 (H) 90 (V) |
| Outer Dimensions | 3.7 (W) x2.3 (H) x 2.3 (D) inches |
| Low Light Enhancement | Infra-Red Lights |
| Lux. Rating | 0.1 lux / IR on 0.001 lux |
| Audio | Built in Microphone |
| Housing | Lightweight Aluminum Die Cast |
| Vibration Rating | 10G |
| Water-proof Camera Cable | 66 ft w/ Water-proof Connectors |